## Slide 1: Object Selection
Student:
Nguyen Van Khoi
Tran Hoang Nam
_______________________
_______________________
Supervisor:
MSc. Tu Trung Hieu

## Slide 2
Introduction
Literature review
Problem statement
Interactive graph cut segmentation
Silent Lazy Snapping solution
Experimental results
Future direction
Question and answer

## Slide 3: Image selection
An image is a set of sub-images that sometimes referred to as regions-of-interest, ROIs, or simply regions.
One of the problem in image processing is image selection – how to cut out or select an area for later specific image processing operations.

## Slide 4: Interactive single-image segmentation
Interactive single-image segmentation (image cutout or foreground/background separation), one of the typical case in region selection problem, is to select the object (e.g. human, flower) from the background that based on samples provided by the user.

## Slide 5: Image segmentation from Lazy Snapping paper

## Slide 6
Introduction
Literature review
Problem statement
Interactive graph cut segmentation
Silent Lazy Snapping solution
Experimental results
Future direction
Question and answer

## Slide 7: Literature review
Greig et al, 1989: the first using min-cut max-flow algorithm to optimize certain energy function in vision.
Boykov and Jolly, 2001: basing on the work of Greig, finding optimal segmentation which satisfies hard constraints imposed by user and soft constraints combining both region and boundary properties.
Li, Tang, Sun and Shum, 2004: improving the method of Boykov and Jolly, working on super-pixel with an extra boundary-editing step.
Rother, Kolgomorov and Blake, 2004: the iterated version of Boykov and Jolly, using color and contrast information with border matting for optimize the boundary.

## Slide 8: Lazy Snapping samples

## Slide 9: GrabCut samples

## Slide 10
Introduction
Literature review
Problem statement
Interactive graph cut segmentation
Silent Lazy Snapping solution
Experimental results
Future direction
Question and answer

## Slide 11: Problem statement
Suppose we have an input image N and some sets of pixels:
Foreground set : set of all pixels that are sample for the object.
Background set : set of all pixels that are sample for the background.
Uncertain set : set of all pixels that are not in the both fore/background set.
How to figure out all pixels belong to the object in the image and separate them from the background?

## Slide 12: Binary images: foreground, background
A binary image is an image in which each pixel belongs to one of only two possible discrete logical value: 1 or 0. In out problem:
  The logical value 1 is known as “object”.
  The logical value 0 is known as “not object”.
We define the set of pixels which logical value is 1/0 as the temp foreground/background pixel.

## Slide 13: Binary labelling problem
For all image pixels, we need to assign a unique label
  If a pixel is in the foreground/background set, the label of it is 1/0.
  If a pixel is not in the foreground and background set, the temporary label of it is “uncertain”.
How to find a way to label all pixels in the image so that all pixels belong to object we want to select have same label, and so do to the another pixel?

## Slide 14: Binary labelling problem - Constraint
Data constraint
If a pixel has it colors similar to at least one pixel belong to foreground seeds, it is more likely to get foreground label, and so do with background seeds.
Prior constraint
Pixels that belong to the object tend to group together, and so do with pixels that belong to background.

## Slide 15: Binary labeling problem
We model data constraint by using Data Penalty Function
To figure out how image satisfy the data constraint, we sum up all pixel penalty function:

## Slide 16: Prior constraint Discontinuity definition
Pixel p and q exist a discontinuity if . By that, each pixel belong to the object boundary have some discontinuities pixels around.

## Slide 17: Binary labeling problem
We model the prior constraint as a function of the color gradient for all discontinuities:
Where:
  is the L2-Norm of RGB color difference between two pixels p and q.

## Slide 18: Binary labelling problem
Minimize the energy function (Greig et al., 1989)
Where know as a balancing parameter between data constraint and the prior constraint:
  The larger lambda, the less discontinuities in the optimal labeling L.
  The smaller lambda, the more optimal labeling L.

## Slide 19
Introduction
Literature review
Problem statement
Interactive graph cut segmentation
Silent Lazy Snapping solution
Experimental results
Future direction
Question and answer

## Slide 20: Energy function

## Slide 21: Graph cut construction
A simple segmentation example for a 3x3 image.

## Slide 22: Energy function (cont.)

## Slide 23: Detailed implementation
Negative log-likelihood of intensity for regional term
Ad hoc function for boundary term
Max-flow algorithm provided by Boykov and Kolgomorov (2001)

## Slide 24: Sample result and comment

## Slide 25
Introduction
Literature review
Problem statement
Interactive graph cut segmentation
Silent Lazy Snapping solution
Experimental results
Future direction
Question and answer

## Slide 26: Silent Lazy Snapping model

## Slide 27: Step 1: Sample definition

## Slide 28: Sample definition step
Sample definition in pixel level:
Blue color: pixel belongs to foreground/object.
Red color: pixel belongs to background.

## Slide 29: Step 2: Pre-segmentation by SEEDs algorithm

## Slide 30: Pre-segmentation step K-means method (4124 segments)
Cannot control the number of segments.
Over-segmentation problem.
Easy to implement, but require time and memory.

## Slide 31: Pre-segmentation step Watershed method (212 segments)
Cannot control the number of segments.
Under-segmentation problem.
Unstable because result depends on threshold value.

## Slide 32: Pre-segmentation step SEEDs – Super pixel (800 segments)
Can control the number of segments.
Depend on the number of iteration.
Under-fitting boundary problem.

## Slide 33: Pre-segmentation step SEEDs – Revised Mean Pixel (800 segments)
Can control the number of segments.
Depend on the number of iteration.
Stable, usable result.

## Slide 34: Comparison between SEEDs Super Pixel and SEEDs Revised Mean Pixel
SEEDs Super Pixel
SEEDs Revised Mean Pixel

## Slide 35: Pre-segmentation step
Segments combine with sample definition in pixel level:
Blue color: pixel belongs to foreground/object.
Red color: pixel belongs to background.

## Slide 36: Step 3: Graph initialization

## Slide 37: Network properties
Network G = (V, E)
V = {source, sink, segments}
  |V| = number of segments + 2
  I(u) = mean value of segment u
E = {t-link, n-link}
  If pixel p with label L[p] is a neighbor of pixel q with label L[q] and L[p] <> L[q], so p and q are neighbor in the network.
  If pixel p belongs to foreground sample, we mark vertex L[p] connect to source.
  If pixel q belongs to background sample, we mark vertex L[q] connect to sink.

## Slide 38: Step 4: Graph cut and final segmentation

## Slide 39: Final segmentation
We apply Graph Cut solution of Yuri Boykov and Vladimir Kolmogorov to the network to solve maximum flow problem.

## Slide 40: Final segmentation
We transfer label value of vertices back to all regions in the original image, change color or background regions to get final segmentation – object selection.

## Slide 41: Sample result

## Slide 42: Limitation 1: Pixel loss in thin area
189080 with samples
Final segmentation

## Slide 43: Limitation 2: Unsmooth boundary
Dancing_Emily with samples
Final segmentation

## Slide 44: Limitation 3: Poor performance when foreground and background have similar color distribution
Vango with samples
Final segmentation

## Slide 45
Introduction
Literature review
Problem statement
Interactive graph cut segmentation
Silent Lazy Snapping solution
Experimental results
Future direction
Question and answer

## Slide 46: Berkeley dataset – 12003.jpg
Interactive Graph Cut
Silent Lazy Snapping

## Slide 47: Berkeley dataset – 35070.jpg
Interactive Graph Cut
Silent Lazy Snapping

## Slide 48: Berkeley dataset – 176035.jpg
Interactive Graph Cut
Silent Lazy Snapping

## Slide 49: Berkeley dataset – 187029.jpg
Interactive Graph Cut
Silent Lazy Snapping

## Slide 50: Berkeley dataset – 207056.jpg
Interactive Graph Cut
Silent Lazy Snapping

## Slide 51: Khoi’s dataset – 5.jpg
Original Image
Interactive Graph Cut

## Slide 52: Khoi’s dataset – 6.jpg
Original Image
Interactive Graph Cut

## Slide 53: Khoi’s dataset – 7.jpg
Original Image
Interactive Graph Cut

## Slide 54: Khoi’s dataset – 8.jpg
Original Image
Interactive Graph Cut

## Slide 55: Khoi’s dataset – 9.jpg
Original Image
Interactive Graph Cut

## Slide 56: Nam’s dataset – Cat.jpg
Original Image
Silent Lazy Snapping

## Slide 57: Nam’s dataset – TrangAn.jpg
Original Image
Silent Lazy Snapping

## Slide 58: Nam’s dataset – Nam_2.jpg
Original Image
Silent Lazy Snapping

## Slide 59: Nam’s dataset – WSpaper.jpg
Original Image
Silent Lazy Snapping

## Slide 60: Nam’s dataset – Emily_child.jpg
Original Image
Silent Lazy Snapping

## Slide 61
Introduction
Literature review
Problem statement
Interactive graph cut segmentation
Silent Lazy Snapping solution
Experimental results
Future direction
Question and answer

## Slide 62
Introduction
Literature review
Problem statement
Interactive graph cut segmentation
Silent Lazy Snapping solution
Experimental results
Future direction
Question and answer

## Slide 63: THANK YOU FOR LISTENING!